## Slide 1: Radiofrequency Pulses in MRI
Mahesh Keerthivasan
BME 639
University of Arizona
Lecture 2

## Slide 2: Review
Adapted from Larry Wald’s slides, fMRI MR Physics
Main
Field
Bo
x
y
z
North
M0
Applied B1 RF Field
B1(t)
x
y
z
M0
The RF pulse rotates Mo the about applied field
B1

## Slide 3: Review
Adapted from MRI from Picture to Proton. Cambridge: Cambridge University Press
High frequency carrier wave modulated by low frequency RF pulse to generate B1 field
Flip angle : controls tip angle of magnetization

## Slide 4: Review
Using Bloch equations and small flip angle approximation we can find the distribution of flip angles across the excited slice
Achieved by measuring the transverse magnetization
Slice profile is approximately equal to inverse Fourier transform of RF pulse

## Slide 5: RF Pulse Slice Profile
Fourier Transform
https://www.chem.purdue.edu/courses/chm621/text/ft/basiset/rect/rect.htm
Flip angle
Ideal slice profile
For a finite slice profile we require an infinite duration sinc pulse !

## Slide 6: RF Pulse Slice Profile
Slice profiles for a 30o RF pulse
(0.523 radians)

## Slide 7: RF Pulse Slice Profile
Slice profiles for a 30o RF pulse
(0.523 radians)

## Slide 8: RF Pulse Slice Profile
Slice profiles for a 30o RF pulse
(0.523 radians)

## Slide 9: RF Pulse Slice Profile
Slice profiles for a 30o RF pulse
(0.523 radians)

## Slide 10: RF Pulse Slice Profile
x
FT
*
Modulation property

## Slide 11: RF Pulse Design: Sinc
Handbook of MRI Pulse Sequences, Bernstein
Sinc function:
: Number of zeros crossing of the sinc
: first zero crossing
Time-Bandwidth product:

## Slide 12: RF Pulse Design: Sinc
Windowed RF Pulse:
Multiple the RF pulse function by an appropriate window function to taper the RF amplitude at the beginning and end
Enable smooth roll off in slice profile
window function w(t)
sinc(t)
Handbook of MRI Pulse Sequences, Bernstein
Notes: - Depending on value of alpha can be Hanning (0.5) or hamming (0.46)

## Slide 13: RF Pulse Design: Sinc
Sinc RF
Windowed Sinc RF

## Slide 14: RF Pulse Design: Hard Pulse
Can we excite the entire volume ?
Bo
Slides from Dr. Nan-kuei Chen
Bo
Notes: Why would we want to excite the entire volume ?

## Slide 15: RF Pulse Design: Hard Pulse
Hard pulses: rectangular shaped RF pulse played without slice select gradients
Needs to have a broad bandwidth to excite spins with wide range of frequencies
Hard pulses are typically few hundred micro-seconds in duration
Flip angle
For an infinite slice profile we require a very narrow RF pulse !
https://www.chem.purdue.edu/courses/chm621/text/ft/basiset/rect/rect.htm

## Slide 16: Simultaneous Multi-slice Excitation
So far, excite multiple slices sequentially by changing RF frequency
Can we excite multiple slices simultaneously ?

## Slide 17: Simultaneous Multi-slice Excitation
Slice profile when exciting one slice
Flip angle
Slice profile when simultaneously exciting two slices
Flip angle
?

## Slide 18: Simultaneous Multi-slice Excitation
Flip angle
+
Flip angle
Flip angle

## Slide 19: Simultaneous Multi-slice Excitation
Fourier Transform Shift property
Multiplication by complex exponential function
Shift in frequency

## Slide 20: Simultaneous Multi-slice Excitation
Flip angle
*
+
Flip angle

## Slide 21: Simultaneous Multi-slice Excitation
Multi-band excitation offers boost in SNR when simultaneously exciting N slices

## Slide 22: Simultaneous Multi-slice Excitation
Interleaved diffusion-weighted improved by adaptive partial-Fourier and multiband multiplexed sensitivity-encoding reconstruction. Magn Reson Med. 2015: 73(5):1872-84.

## Slide 23: Simultaneous Multi-slice Excitation
Interleaved EPI based fMRI improved by multiplexed sensitivity encoding (MUSE) and simultaneous multi-band imaging. PLoS One. 2014 Dec 30;9(12):e116378
Interleaved EPI based fMRI improved by multiplexed sensitivity encoding (MUSE) and simultaneous multi-band imaging. PLoS One. 2014 Dec 30;9(12):e116378
Interleaved EPI based fMRI improved by multiplexed sensitivity encoding (MUSE) and simultaneous multi-band imaging. PLoS One. 2014 Dec 30;9(12):e116378

## Slide 24: RF Design: VERSE
Can the slice select gradient be time varying ?
Variable rate selective excitation (VERSE) : RF pulse with time varying slice select gradient
Used to reduce RF power deposition by decreasing RF amplitude at the peak of pulse
Gs
Gs
Notes: - Z related to resonant frequency

## Slide 25: RF Design: VERSE
Handbook of MRI Pulse Sequences, Bernstein
Notes: - Z related to resonant frequency

## Slide 26: RF Design: VERSE
Duration of VR pulse increased to maintain flip angle
This reduces RF bandwidth of portion that is stretched
Slice select gradient is reduced to maintain same slice profile
: reduction factor in RF amplitude
Handbook of MRI Pulse Sequences, Bernstein
Notes: - Z related to resonant frequency

## Slide 27: RF Design: SLR
Interleaved EPI based fMRI improved by multiplexed sensitivity encoding (MUSE) and simultaneous multi-band imaging. PLoS One. 2014 Dec 30;9(12):e116378
Interleaved EPI based fMRI improved by multiplexed sensitivity encoding (MUSE) and simultaneous multi-band imaging. PLoS One. 2014 Dec 30;9(12):e116378
Given a slice profile can we design the corresponding RF pulse ?
For small flip angles < 30o the inverse Fourier transform can be used
For larger flip angles SLR algorithm (Shinnar-Le Roux)
Hard pulse approximation
Handbook of MRI Pulse Sequences, Bernstein

## Slide 28: RF Design: SLR
Interleaved EPI based fMRI improved by multiplexed sensitivity encoding (MUSE) and simultaneous multi-band imaging. PLoS One. 2014 Dec 30;9(12):e116378
Interleaved EPI based fMRI improved by multiplexed sensitivity encoding (MUSE) and simultaneous multi-band imaging. PLoS One. 2014 Dec 30;9(12):e116378
Effect of RF pulse on magnetization can be characterized by a rotation matrix:
Handbook of MRI Pulse Sequences, Bernstein
: Cayley-Klein parameters
Captures non-linearities of Bloch equations
Ignores relaxation effects

## Slide 29: RF Design: SLR
Interleaved EPI based fMRI improved by multiplexed sensitivity encoding (MUSE) and simultaneous multi-band imaging. PLoS One. 2014 Dec 30;9(12):e116378
Interleaved EPI based fMRI improved by multiplexed sensitivity encoding (MUSE) and simultaneous multi-band imaging. PLoS One. 2014 Dec 30;9(12):e116378
Forward SLR Transform:
Using hard pulse approximation decompose effect of shaped RF pulse to series of rotations
Final magnetization is result of multiplying the individual rotation matrices
Series of hard pulses produce same flip angle as soft pulse
Handbook of MRI Pulse Sequences, Bernstein

## Slide 30: RF Design: SLR
Interleaved EPI based fMRI improved by multiplexed sensitivity encoding (MUSE) and simultaneous multi-band imaging. PLoS One. 2014 Dec 30;9(12):e116378
Interleaved EPI based fMRI improved by multiplexed sensitivity encoding (MUSE) and simultaneous multi-band imaging. PLoS One. 2014 Dec 30;9(12):e116378
Forward SLR Transform:
Recursively decompose nutation and precession effect of RF pulse to two complex polynomials
Polynomials are related to Cayley-Klein parameters
Use the rotation matrix representation to compute the resultant magnetization
Handbook of MRI Pulse Sequences, Bernstein
Notes: - Z related to resonant frequency

## Slide 31: RF Design: SLR
Inverse SLR Transform:
Generate the polynomials based on the desired slice profile using Parks- McClellan algorithm
  Flip angle, percent ripple in passband and stopband
Translate the two polynomials to the individual RF pulse elements recursively
Allows recovery of entire hard pulse approximation
Handbook of MRI Pulse Sequences, Bernstein
45o flip angle RF pulse with 2% ripple in passband and stopband
Notes: - Z related to resonant frequency

## Slide 32: RF Design: Excitation k-space
Back to the small tip angle approximation :
      where,
Excitation k-space
Describes a path through spatial frequency space
John Pauly, A k-space analysis of small tip angle excitation, 1989

## Slide 33: RF Design: Excitation k-space
John Pauly, A k-space analysis of small tip angle excitation, 1989
Location in k-space at time is integral of remaining gradient waveform
Reach origin of k-space halfway through positive lobe of gradient
Refocusing lobe brings back to origin

## Slide 34: RF Design: Excitation k-space
RF design involves selecting:
  the magnetization response (slice profile)
  the excitation k-space trajectory
Rate of excitation k-space traversal
Sampling density correction
G
This method works for flip angles upto 90o

## Slide 35: RF Design: 2D RF
Handbook of MRI Pulse Sequences, Bernstein
Two dimensional excitation

## Slide 36: RF Design: 2D RF
2D Excitation Profile
K-space trajectory and Gradient waveform
RF Pulse
John Pauly, A k-space analysis of small tip angle excitation, 1989
EE469B: RF Pulse Design for MRI, Stanford University
Handbook of MRI Pulse Sequences, Bernstein
K-space trajectory

## Slide 37: RF Design: 2D RF
A Cylindrical, Inner Volume Selecting 2D-T2-Prep Improves GRAPPA-Accelerated Image Quality in MRA of the Right Coronary Artery. Andrew J. Coristine, Jerome Yerly, Matthias Stuber , Plos One, October 2016

## Slide 38: RF Design: 2D RF
Mitsouras D, Mulkern RV, Rybicki FJ. Strategies for inner volume 3D fast spin echo magnetic resonance imaging using non-selective refocusing radio frequency pulses. Medical physics. 2006;33(1):173-186.